## Slide 1: Chapter 3: VLANs
Routing & Switching
Notes: Cisco Networking Academy program
Routing & Switching
Chapter 3: VLANs

## Slide 2: Chapter 3
3.1 VLAN Segmentation
3.2 VLAN Implementation
3.3 VLAN Security and Design
3.4 Summary
Notes: Chapter 3

## Slide 3: Chapter 3: Objectives
Explain the purpose of VLANs in a switched network.
Analyze how a switch forwards frames based on VLAN configuration in a multi-switched environment.
Configure a switch port to be assigned to a VLAN based on requirements.
Configure a trunk port on a LAN switch.
Configure Dynamic Trunk Protocol (DTP).
Troubleshoot VLAN and trunk configurations in a switched network.
Configure security features to mitigate attacks in a VLAN-segmented environment.
Explain security best practices for a VLAN-segmented environment.
Notes: Chapter 3 Objectives

## Slide 4: 3.1 VLAN Segmentation
Notes: Cisco Networking Academy program
Routing & Switching
Chapter 3: VLANs

## Slide 5: Overview of VLANs VLAN Definitions
A VLAN is a logical partition of a Layer 2 network.
Multiple partitions can be created, allowing for multiple VLANs to co-exist.
Each VLAN is a broadcast domain, usually with its own IP network.
VLANs are mutually isolated and packets can only pass between them via a router.
The partitioning of the Layer 2 network takes place inside a Layer 2 device, usually via a switch.
The hosts grouped within a VLAN are unaware of the VLAN’s existence.
Notes: 3.1.1.1 VLAN Definitions

## Slide 6: Overview of VLANs VLAN Definitions (cont.)
Notes: 3.1.1.1 VLAN Definitions

## Slide 7: Overview of VLANs Benefits of VLANs
Security
Cost reduction
Better performance
Shrink broadcast domains
Improved IT staff efficiency
Simpler project and application management
Notes: 3.1.1.2 Benefits of VLANs

## Slide 8: Overview of VLANs Types of VLANs (cont.)
Notes: 3.1.1.3 Types of VLANs

## Slide 9: VLANs in a Multi-Switched Environment VLAN Trunks
A VLAN trunk carries more than one VLAN.
A VLAN trunk is usually established between switches so same-VLAN devices can communicate, even if physically connected to different switches.
A VLAN trunk is not associated to any VLANs; neither is the trunk ports used to establish the trunk link.
Cisco IOS supports IEEE802.1q, a popular VLAN trunk protocol.
Notes: 3.1.2.1 VLAN Trunks

## Slide 10: VLANs in a Multi-Switched Environment VLAN Trunks (cont.)
Notes: 3.1.2.1 VLAN Trunks

## Slide 11: VLANs in a Multi-Switched Environment Controlling Broadcast Domains with VLANs
VLANs can be used to limit the reach of broadcast frames.
A VLAN is a broadcast domain of its own.
A broadcast frame sent by a device in a specific VLAN is forwarded within that VLAN only.
VLANs help control the reach of broadcast frames and their impact in the network.
Unicast and multicast frames are forwarded within the originating VLAN.
Notes: 3.1.2.2 Controlling Broadcast Domains with VLANs

## Slide 12: VLANs in a Multi-Switched Environment Tagging Ethernet Frames for VLAN Identification
Frame tagging is the process of adding a VLAN identification header to the frame.
It is used to properly transmit multiple VLAN frames through a trunk link.
Switches tag frames to identify the VLAN to that they belong. Different tagging protocols exist; IEEE 802.1Q is a vey popular example.
The protocol defines the structure of the tagging header added to the frame.
Switches add VLAN tags to the frames before placing them into trunk links and remove the tags before forwarding frames through nontrunk ports.
When properly tagged, the frames can transverse any number of switches via trunk links and still be forwarded within the correct VLAN at the destination.
Notes: 3.1.2.3 Tagging Ethernet Frames for VLAN Identification

## Slide 13: VLANs in a Multi-Switched Environment Tagging Ethernet Frames for VLAN Identification
Notes: 3.1.2.3 Tagging Ethernet Frames for VLAN Identification

## Slide 14: 3.2 VLAN Implementations
Notes: Cisco Networking Academy program
Routing & Switching
Chapter 3: VLANs

## Slide 15: VLAN Assignment VLAN Ranges on Catalyst Switches
Cisco Catalyst 2960 and 3560 Series switches support over 4,000 VLANs.
VLANs are split into two categories:
  Normal range VLANs
    VLAN numbers from 1 to 1,005
    Configurations stored in the vlan.dat (in the flash memory)
    VTP can only learn and store normal range VLANs
  Extended Range VLANs
    VLAN numbers from 1,006 to 4,096
    Configurations stored in the running configuration (NVRAM)
    VTP does not learn extended range VLANs
Notes: 3.2.1.1 VLAN Ranges On Catalyst Switches

## Slide 16: VLAN Assignment Creating a VLAN
Notes: 3.2.1.2 Creating a VLAN

## Slide 17: VLAN Assignment Assigning Ports to VLANs
Notes: 3.2.1.3 Assigning Ports To VLANs

## Slide 18: VLAN Assignment Assigning Ports to VLANs (cont.)
Notes: 3.2.1.3 Assigning Ports To VLANs

## Slide 19: VLAN Assignment Changing VLAN Port Membership
Notes: 3.2.1.4 Changing VLAN Port Membership

## Slide 20: VLAN Assignment Changing VLAN Port Membership (cont.)
Notes: 3.2.1.4 Changing VLAN Port Membership

## Slide 21: VLAN Assignment Deleting VLANs
Notes: 3.2.1.5 Deleting VLANs

## Slide 22: VLAN Assignment Verifying VLAN Information
Notes: 3.2.1.6 Verifying VLAN Information

## Slide 23: VLAN Assignment Verifying VLAN Information (cont.)
Notes: 3.2.1.6 Verifying VLAN Information

## Slide 24: VLAN Assignment Configuring IEEE 802.1q Trunk Links
Notes: 3.2.2.1 Configuring IEEE 802.1q Trunk Links

## Slide 25: VLAN Assignment Resetting the Trunk To Default State
Notes: 3.2.2.2 Resetting the Trunk To Default State

## Slide 26: VLAN Assignment Resetting the Trunk To Default State (cont.)
Notes: 3.2.2.2 Resetting the Trunk To Default State

## Slide 27: VLAN Assignment Verifying Trunk Configuration
Notes: 3.2.2.3 Verifying Trunk Configuration

## Slide 28: Dynamic Trunking Protocol Introduction to DTP
Switch ports can be manually configured to form trunks.
Switch ports can also be configured to negotiate and establish a trunk link with a connected peer.
The Dynamic Trunking Protocol (DTP) manages trunk negotiation.
DTP is a Cisco proprietary protocol and is enabled, by default, in Cisco Catalyst 2960 and 3560 switches.
If the port on the neighbor switch is configured in a trunk mode that supports DTP, it manages the negotiation.
The default DTP configuration for Cisco Catalyst 2960 and 3560 switches is dynamic auto.
Notes: 3.2.3.1 Introduction to DTP

## Slide 29: Dynamic Trunking Protocol Negotiated Interface Modes
Cisco Catalyst 2960 and 3560 support the following trunk modes:
  Switchport mode dynamic auto
  Switchport mode dynamic desirable
  Switchport mode trunk
  Switchport nonegotiate
Notes: 3.2.3.2 Introduction to DTP

## Slide 30: Troubleshooting VLANs and Trunks IP Addressing Issues with VLAN
It is a common practice to associate a VLAN with an IP network.
Because different IP networks only communicate through a router, all devices within a VLAN must be part of the same IP network to communicate.
The figure displays that PC1 cannot communicate to the server because it has a wrong IP address configured.
Notes: 3.2.4.1 IP Addressing Issues with VLAN

## Slide 31: Troubleshooting VLANs and Trunks Missing VLANs
If all the IP addresses mismatches have been solved, but the device still cannot connect, check if the VLAN exists in the switch.
Notes: 3.2.4.2 Missing VLANs

## Slide 32: Troubleshooting VLANs and Trunks Introduction to Troubleshooting Trunks
Notes: 3.2.4.3 Introduction to Troubleshooting Trunks

## Slide 33: Troubleshooting VLANs and Trunks Common Problems with Trunks
Trunking issues are usually associated with incorrect configurations.
The most common type of trunk configuration errors are:
  Native VLAN mismatches
  Trunk mode mismatches
  Allowed VLANs on trunks
If a trunk problem is detected, the best practice guidelines recommend to troubleshoot in the order shown above.
Notes: 3.2.4.4 Common Problems With Trunks

## Slide 34: Troubleshooting VLANs and Trunks Trunk Mode Mismatches
If a port on a trunk link is configured with a trunk mode that is incompatible with the neighboring trunk port, a trunk link fails to form between the two switches.
Use the show interfaces trunk command to check the status of the trunk ports on the switches.
To fix the problem, configure the interfaces with proper trunk modes.
Notes: 3.2.4.5 Trunk Mode Mismatches

## Slide 35: Troubleshooting VLANs and Trunks Incorrect VLAN List
VLANs must be allowed in the trunk before their frames can be transmitted across the link.
Use the switchport trunk allowed vlan command to specify which VLANs are allowed in a trunk link.
Use the show interfaces trunk command to ensure the correct VLANs are permitted in a trunk.
Notes: 3.2.4.6 Incorrect VLAN List